## Slide 1: Quality Analysis of Onions Literature Survey

## Slide 2: Summary
Classification is mainly done with convolutional neural network-based analysis on onion image data.
Features considered: Colour, Size, Shape, etc.
Literature for onion classification is not broader.
Other fruits and vegetables classification using deep learning models is available.
Few literature with respect to onions are given below

## Slide 3: A multimodal machine vision system for quality inspection of onion, W. Wang, C. Li (Journal of food engineering, 2015)
Comprehensive evaluation of the quality of onions
A hardware implementable model is developed
Colour imaging – spatial and colour information of onions
Spectral imaging – to examine surface blemish and rot of onion
RGB-D sensor – measure size and geometry information of onions
X-ray imaging – to detect internal defects and disease infections in onions
Colour image camera: GigE Vision camera (1400 x 1200 pixels, 12 fps)
RGB-depth sensor: depth images (640 x 480 pixels, 30fps)
Colour camera and RGB-D sensor to acquire colour and depth images
Spectral images of onions
X-ray line scanner

## Slide 4: Artificial Intelligence for Agriculture: A technique of vegetable crop onion sorting and grading using deep learning, A. Paymode, et. al. (2021, International journal of advanced scientific research and engineering trends)
Sorting and Grading – based on size, quality and shapes
Size: small, medium, large, extra-large
Weights: 115gms, 170gms, 285gms, 454gms
Diameter: 1 inch to 4 inch
LabView software: colour of images, spectral images and depth of onions
Dataset: 104 healthy, 96 unhealthy, include different size, colour, and single or group
Data Augmentation: to automatically expand the size of training dataset
CNN based classification model
Hyper-parameters tuning for improvement in the model results

## Slide 5: Cluster analysis and artificial neural networks multivariate classification of onion varieties, B. Galdon, et. al. (2010, Journal of Agriculture and food chemistry)
Image processing algorithms: Canny Edge method, Color masking, Pixel per metric ratio, RGB method, Blob method
Features: Size, colour, texture of bulbs
Classification: small, medium, large, jumbo

## Slide 6: Deep learning for classifying types of onions using Google colab, M.Alijla (2021, International Journal of Academic Engineering Research)
CNN architecture for image classification
Dataset: 1333 onion images
Categories: A) Onion white(438) B) Onion Red Peeled(445) C) Onion Red(450)
Development and performance evaluation of a manually operated grading machine, K. Umani, et. al. (2020, Journal of agriculture and food research, Elsevier)
Developed manual operated grading machine for three sizes (0-40,40-60,>60 mm)
Dataset: 1333 onion images
Categories: A) Onion white(438) B) Onion Red Peeled(445) C) Onion Red(450)